# CH Comm 3.0.0

##### User’s guide for CH Comm

Claude Hanssens

# Basic Description of CH Comm

This program has been developed for use with Microsoft® Flight Simulator® 2000.

CH Comm will read information from Microsoft® Flight Simulator® 2000. The information is then formatted into a standard bytestream and sent to one of the serial ports of the user's computer.

CH Comm is also able to read a standard bytestream from a serial port and write that information to Microsoft® Flight Simulator® 2000.

CH Comm cannot be used stand-alone:

- it must be installed on a computer running Microsoft® Flight Simulator® 2000

and

- it must be connected using the serial port

- to another computer running certain software

or

- to specific electronic components

The description of the bytestreams used as output and input is included in this document.

A user can connect to the serial port:

- another computer running certain software

- specific electronic components

If a computer is connected to the serial port, users can use the received bytestream and program their own add-on: virtual instruments, cockpit, ...

If electronic components are connected to the serial port, a user can use the received bytestream and control virtual instruments or controls: throttle, ...

# Version and Upgrade

Actual version of CH Comm is 3.0.0.

There will be upgrades to this version.

These upgrades can be minor upgrades, major upgrades or a fully new version.

## History

Version 1 and 2 have not been distributed and were development versions. Version 3 is the first released version.

# Distribution

CH Programs are available for download from the Internet.

More information can be found in the following chapters:

- Disclaimer

- Redistribution terms

- Copyright

# Requirements

The CH Comm must be installed on a computer running Microsoft® Flight Simulator® 2000.

To use CH Comm, FSUIPC from Pete Dowson must be installed. FSUIPC is freely available from the site www.schiratti.com. FSUIPC is not installed by CH Comm’s setup program.

# Installation

## CH Comm

If you have any previous version of the CH Comm, you must uninstall it before installing a newer version. To uninstall CH Comm:

- Click Start-Settings-Control Panel-Add/Remove programs

- Click on “CH Comm”, if it is in the list.

- Click on the "Remove" button.

To install CH Comm, unzip the archive file in a temporary folder and simply run the “Setup” program in the temporary folder.

The Setup will ask you a destination folder. You can choose any folder (e.g.: “C:\CH”); it is not required that the CH Comm folder is a subfolder of Microsoft® Flight Simulator® 2000.

After installing CH Comm, you may have to restart your computer.

# User’s guide

## General

CH Comm cannot be used alone. You must connect another device to the serial port. This device can be

- another computer

- electronic components

If a computer is connected to the serial port, users can use the received bytestream and program their own add-on. For example, a program running on the connected computer can display the received information in various formats: display similar to EICAS or similar to gauges. The program running on the connected computer too can send info to Microsoft® Flight Simulator® 2000 via CH Comm. It is possible to build an additional panel to control some specific functions of Microsoft® Flight Simulator® 2000.

If electronic components are connected to the serial port, the user can use the received bytestream and control virtual instruments or controls. For example, the electronic equipment connected can transform the received bytestream into AC or DC and turn LEDs on and off. You can connect potentiometers to the electronic components to build throttles.

## User Interface of CH Comm

The user interface of CH Comm is very basic. You only use it to connect to Microsoft® Flight Simulator® 2000 and to open a serial port. You can change most of the parameters of CH Comm using the ini-file.

When you start CH Comm, the interface looks like the picture below:

It has the following areas:

- Connect to FS: Microsoft® Flight Simulator® 2000 must already be running on the local computer.

- Comm Settings: see below.

- Connect to Comm.

- About: will display the “About screen”.

To start the process:

- Start Microsoft® Flight Simulator® 2000

- In the Start-Programs menu, click on the icon CH Comm

- Click on “Connect to FS”

- CH Comm will display a message saying that you are connected to FS

- Click on “Connect to Comm”

- Minimise the CH Comm and fly normally.

The program will work in the background.

If Microsoft® Flight Simulator® 2000 stops or crashes, the CH Comm will stop automatically.

### Comm Settings Area

The Comm Settings area is read-only. The settings can be adapted in the ini-file in the section ComSettings.

The Comm Settings area displays the following information:

- Port: the serial port used.

- Settings: the settings used for the serial port

- Timer: the interval at which data is sent to the serial port

- Data: will blink to show that data is sent or received at the serial port

## CH Comm Modes

### General

Actually, CH Comm can send data in one mode and receive data in 3 different modes. These modes are described in this chapter.

You can use the Output mode and one Input mode at the same time.

Input modes can be set in the ini-file.

The bytestream is always fixed length string.

### Output mode

In Output mode, data is sent to the serial port on a timed basis. The interval can be specified in the ini-file by setting the parameter Timer.

You can choose what data you want to send to the serial port by setting each individual parameter in the ini-file to 1 (output only) or to 3 (output and input).

CH Comm will then send a formatted bytestream containing the data to the serial port.

The following table describes the output format.

| Start | Length | INI Setting | Description | Remark |
| --- | --- | --- | --- | --- |
| 1 | 1 | BOF | Start of message | Default: underscore. Can be adapted |
| 2 | 2 | FSTime | Hours | Hours |
| 4 | 2 | FSTime | Minutes | Minutes |
| 6 | 2 | FSTime | Seconds | Seconds |
| 8 | 4 | Coordinate | Latitude | 1st char = + (N) or - (S); 3 chars for degrees |
| 12 | 1 | Coordinate | Latitude | Decimal separator; can change according to the user’s Regional Settings |
| 13 | 6 | Coordinate | Latitude | Decimal part |
| 19 | 4 | Coordinate | Longitude | 1st char = + (W) or - (E); 3 chars for degrees |
| 23 | 1 | Coordinate | Longitude | Decimal separator; can change according to the user’s Regional Settings |
| 24 | 6 | Coordinate | Longitude | Decimal part |
| 30 | 5 | MSL | Altitude MSL | In feet |
| 35 | 5 | AGL | Altitude AGL | In feet (Read-only) |
| 40 | 4 | Pitch | Pitch | 1st char = + or - ; 3 chars for degrees |
| 44 | 4 | Bank | Bank | 1st char = + or -; 3 chars for degrees |
| 48 | 3 | Heading | Heading | In degrees |
| 51 | 3 | Speed | True airspeed | In knots (Read only) |
| 54 | 3 | Speed | Indicated airspeed | In knots (Read only) |
| 57 | 5 | Vspeed | Vertical speed | 1st char = + or - ; 4 chars for feet (Read only) |
| 62 | 6 | Elevator | Elevator | From -16383 (down) to +16383 (up) |
| 68 | 6 | Aileron | Aileron | From -16383 (left) to +16383 (right) |
| 74 | 6 | Rudder | Rudder | From -16383 (left) to +16383 (right) |
| 80 | 6 | ElevTrim | Elevator Trim | From -16383 (down) to +16383 (up) |
| 86 | 6 | AilTrim | Aileron Trim | From -16383 (up) to +16383 (down) |
| 92 | 6 | RudTrim | Rudder Trim | From -16383 (left) to +16383 (right) |
| 98 | 5 | Flaps | Flaps | From 0 (up) to 16383 (down) |
| 103 | 5 | Spoiler | Spoiler | 0 (in), 4800 (armed), 16383 (extended) |
| 108 | 1 | Gear | Gear | 0 (up) or 16383 (down) |
| 109 | 5 | Brakes | Left Brake | From 0 (off) to 16383 (full) |
| 114 | 5 | Brakes | Right Brake | From 0 (off) to 16383 (full) |
| 119 | 1 | Brakes | Parking Brake | 0 (off) or 1 (on) |
| 120 | 1 | Lights | Logo light | 0 (off) or 1 (on) |
| 121 | 1 | Lights | Wing light | 0 (off) or 1 (on) |
| 122 | 1 | Lights | Recognition | 0 (off) or 1 (on) |
| 123 | 1 | Lights | Panel light | 0 (off) or 1 (on) |
| 124 | 1 | Lights | Strobe light | 0 (off) or 1 (on) |
| 125 | 1 | Lights | Taxi light | 0 (off) or 1 (on) |
| 126 | 1 | Lights | Landing light | 0 (off) or 1 (on) |
| 127 | 1 | Lights | Beacon light | 0 (off) or 1 (on) |
| 128 | 1 | Lights | Navigation light | 0 (off) or 1 (on) |
| 129 | 1 | Pitot | Pitot heat | 0 (off) or 1 (on) |
| 130 | 3 | Comm | Comm Freq | First 3 digits |
| 133 | 1 | Comm | Comm Freq | Decimal separator; can change according to the user’s Regional Settings |
| 134 | 2 | Comm | Comm Freq | Decimal part |
| 136 | 3 | Nav1 | Nav 1 Freq | 3 digits |
| 139 | 1 | Nav1 | Nav 1 Freq | Decimal separator; can change according to the user’s Regional Settings |
| 140 | 2 | Nav1 | Nav 1 Freq | Decimal part |
| 142 | 3 | Nav1 | OBS 1 | In degrees |
| 145 | 4 | Nav1 | Loc 1 deviation | From –127 (left) to +127 (right) (Read-only) |
| 149 | 4 | Nav1 | GS deviation | From –127 (up) to +127 (down) (Read-only) |
| 153 | 1 | Nav1 | Vor 1 Flag | 0 (off), 1 (to) or 2 (from) (Read-only) |
| 154 | 3 | Nav2 | Nav 2 Freq | 3 digits |
| 157 | 1 | Nav2 | Nav 2 Freq | Decimal separator; can change according to the user’s Regional Settings |
| 158 | 2 | Nav2 | Nav 2 Freq | Decimal part |
| 160 | 3 | Nav2 | OBS 2 | In degrees |
| 163 | 4 | Nav2 | Loc 2 deviation | From –127 (left) to +127 (right) (Read-only) |
| 167 | 1 | Nav2 | Vor 2 Flag | 0 (off), 1 (to) or 2 (from) (Read-only) |
| 168 | 4 | ADF | ADF Freq | 4 digits |
| 172 | 1 | ADF | ADF Freq | Decimal separator; can change according to the user’s Regional Settings |
| 173 | 1 | ADF | ADF Freq | Decimal part |
| 174 | 3 | ADF | ADF Heading | In degrees (Read-only) |
| 177 | 4 | XPDR | XPDR | 4 digits |
| 181 | 1 | Marker | Inner marker | 0 (off) or 1 (on) (Read-only) |
| 182 | 1 | Marker | Middle marker | 0 (off) or 1 (on) (Read-only) |
| 183 | 1 | Marker | Outer marker | 0 (off) or 1 (on) (Read-only) |
| 184 | 1 | Autopilot | AP Master Switch | 0 (off) or 1 (on) |
| 185 | 1 | Autopilot | AP Wing Leveler | 0 (off) or 1 (on) |
| 186 | 1 | Autopilot | AP Attitude hold | 0 (off) or 1 (on) |
| 187 | 1 | Autopilot | AP Yaw damper | 0 (off) or 1 (on) |
| 188 | 1 | Autopilot | AP Altitude hold | 0 (off) or 1 (on) |
| 189 | 5 | Autopilot | AP Altitude | In feet |
| 194 | 1 | Autopilot | AP Heading hold | 0 (off) or 1 (on) |
| 195 | 3 | Autopilot | AP Heading | In degrees |
| 198 | 1 | Autopilot | AP Nav 1 hold | 0 (off) or 1 (on) |
| 199 | 1 | Autopilot | AP Glideslope | 0 (off) or 1 (on) |
| 200 | 1 | Autopilot | AP Localizer | 0 (off) or 1 (on) |
| 201 | 1 | Autopilot | AP Backcourse | 0 (off) or 1 (on) |
| 202 | 1 | Autopilot | AP Autothrottle | 0 (off) or 1 (on) |
| 203 | 1 | Autopilot | AP TO/GA | 0 (off) or 1 (on) |
| 204 | 1 | Autopilot | AP Airspeed hold | 0 (off) or 1 (on) |
| 205 | 3 | Autopilot | AP Airspeed | In knots |
| 208 | 1 | Autopilot | AP Mach hold | 0 (off) or 1 (on) |
| 209 | 1 | Autopilot | AP Mach | In Mach |
| 210 | 1 | Autopilot | AP Mach | Decimal separator; can change according to the user’s Regional Settings |
| 211 | 2 | Autopilot | AP Mach | Decimal part |
| 213 | 5 | Autopilot | AP Vertical speed | 1st char = + or - ; 4 chars for feet |
| 218 | 4 | Throttle | Throttle 1 | In percent; 1st char = + or -; negative = reverse |
| 222 | 4 | Throttle | Throttle 2 | In percent; 1st char = + or -; negative = reverse |
| 226 | 4 | Throttle | Throttle 3 | In percent; 1st char = + or -; negative = reverse |
| 230 | 4 | Throttle | Throttle 4 | In percent; 1st char = + or -; negative = reverse |
| 234 | 3 | Prop | Prop 1 | In percent |
| 237 | 3 | Prop | Prop 2 | In percent |
| 240 | 3 | Prop | Prop 3 | In percent |
| 243 | 3 | Prop | Prop 4 | In percent |
| 246 | 3 | Mixture | Mixture 1 | In percent |
| 249 | 3 | Mixture | Mixture 2 | In percent |
| 252 | 3 | Mixture | Mixture 3 | In percent |
| 255 | 3 | Mixture | Mixture 4 | In percent |
| 258 | 1 | Magneto | Magneto 1 | 0 (off), 1 (right/start), 2 (left), 3 (both) or 4 (start) |
| 259 | 1 | Magneto | Magneto 2 | 0 (off), 1 (right/start), 2 (left), 3 (both) or 4 (start) |
| 260 | 1 | Magneto | Magneto 3 | 0 (off), 1 (right/start), 2 (left), 3 (both) or 4 (start) |
| 261 | 1 | Magneto | Magneto 4 | 0 (off), 1 (right/start), 2 (left), 3 (both) or 4 (start) |
| 262 | 3 | EngValuesProp | RPM 1 | In percent (Read only) |
| 265 | 3 | EngValuesProp | RPM 2 | In percent (Read only) |
| 268 | 3 | EngValuesProp | RPM 3 | In percent (Read only) |
| 271 | 3 | EngValuesProp | RPM 4 | In percent (Read only) |
| 274 | 2 | EngValuesProp | Manifold pressure 1 | In inches (Read only) |
| 276 | 1 | EngValuesProp | Manifold pressure 1 | Decimal separator; can change according to the user’s Regional Settings |
| 277 | 2 | EngValuesProp | Manifold pressure 1 | Decimal part (Read only) |
| 279 | 2 | EngValuesProp | Manifold pressure 2 | In inches (Read only) |
| 281 | 1 | EngValuesProp | Manifold pressure 2 | Decimal separator; can change according to the user’s Regional Settings |
| 282 | 2 | EngValuesProp | Manifold pressure 2 | Decimal part (Read only) |
| 284 | 2 | EngValuesProp | Manifold pressure 3 | In inches (Read only) |
| 286 | 1 | EngValuesProp | Manifold pressure 3 | Decimal separator; can change according to the user’s Regional Settings |
| 287 | 2 | EngValuesProp | Manifold pressure 3 | Decimal part (Read only) |
| 289 | 2 | EngValuesProp | Manifold pressure 4 | In inches (Read only) |
| 291 | 1 | EngValuesProp | Manifold pressure 4 | Decimal separator; can change according to the user’s Regional Settings |
| 292 | 2 | EngValuesProp | Manifold pressure 4 | Decimal part (Read only) |
| 294 | 2 | EngValuesProp | Oil Pressure 1 | 2 digits (Read only) |
| 296 | 2 | EngValuesProp | Oil Pressure 2 | 2 digits (Read only) |
| 298 | 2 | EngValuesProp | Oil Pressure 3 | 2 digits (Read only) |
| 300 | 2 | EngValuesProp | Oil Pressure 4 | 2 digits (Read only) |
| 302 | 3 | EngValuesProp | Oil Temperature 1 | 3 digits (Read only) |
| 305 | 3 | EngValuesProp | Oil Temperature 2 | 3 digits (Read only) |
| 308 | 3 | EngValuesProp | Oil Temperature 3 | 3 digits (Read only) |
| 311 | 3 | EngValuesProp | Oil Temperature 4 | 3 digits (Read only) |
| 314 | 3 | EngValuesJet | N1 1 | In percent (Read only) |
| 317 | 3 | EngValuesJet | N1 2 | In percent (Read only) |
| 320 | 3 | EngValuesJet | N1 3 | In percent (Read only) |
| 323 | 3 | EngValuesJet | N1 4 | In percent (Read only) |
| 326 | 3 | EngValuesJet | N2 1 | In percent (Read only) |
| 329 | 3 | EngValuesJet | N2 2 | In percent (Read only) |
| 332 | 3 | EngValuesJet | N2 3 | In percent (Read only) |
| 335 | 3 | EngValuesJet | N2 4 | In percent (Read only) |
| 338 | 2 | EngValuesJet | Oil Pressure 1 | 2 digits (Read only) |
| 340 | 2 | EngValuesJet | Oil Pressure 2 | 2 digits (Read only) |
| 342 | 2 | EngValuesJet | Oil Pressure 3 | 2 digits (Read only) |
| 344 | 2 | EngValuesJet | Oil Pressure 4 | 2 digits (Read only) |
| 346 | 3 | EngValuesJet | Oil Temperature 1 | 3 digits (Read only) |
| 349 | 3 | EngValuesJet | Oil Temperature 2 | 3 digits (Read only) |
| 352 | 3 | EngValuesJet | Oil Temperature 3 | 3 digits (Read only) |
| 355 | 3 | EngValuesJet | Oil Temperature 4 | 3 digits (Read only) |
| 358 | 3 | Fuel | External 1 | In percent |
| 361 | 3 | Fuel | Fuel left tip | In percent |
| 364 | 3 | Fuel | Fuel left aux | In percent |
| 367 | 3 | Fuel | Fuel left main | In percent |
| 370 | 3 | Fuel | Center 2 | In percent |
| 373 | 3 | Fuel | Center | In percent |
| 376 | 3 | Fuel | Center 3 | In percent |
| 379 | 3 | Fuel | Fuel right main | In percent |
| 382 | 3 | Fuel | Fuel right aux | In percent |
| 385 | 3 | Fuel | Fuel right tip | In percent |
| 388 | 3 | Fuel | External 2 | In percent |
| 391 | 1 | EOF | End of message | Actually underscore. Can be adapted |

Output bytestream sample:

The data corresponds to the default start-up flight in Microsoft(r) Flight Simulator(r) 2000. All parameters in CH Comm.ini have been set to 1.

_132738+041,853602-087,6074850059400000-004+000360000000+0000+03614-00001-00001-00001+00000+00000000000000016383163821638210000000000127,30110,50360+000+0000113,90360+00000414,0314120000000000000000000000000000000,00+0000+000+000+000+000100000000000100000000000300002600000000005,2200,0000,0000,002700000004300000000002600000000002600000000027000000043000000000100100100100100100100100100100100_

### Input modes

You can use only one Input mode at a time.

The Input mode can be set in the ini-file by setting the parameter Inputmode.

You cannot change the Input mode without closing and restarting CH Comm.

#### Full Data Mode

In this mode, CH Comm waits for bytestreams containing all data. This mode is similar to the output mode.

To use the Full Data mode, set Inputmode to 1.

You can choose what data you want to send to Microsoft(r) Flight Simulator(r) 2000 via the serial port by setting each individual parameter in the ini-file to 2 (input only) or to 3 (output and input).

The bytestream of the Full Data mode is the same as the bytestream for the Output mode.

Read-only data are never part of the input bytestream.

Input in Full Data mode bytestream sample:

All parameters in section [Radio] of CH Comm.ini have been set to 1.

_118.25109.35275117.950901174.97000_

#### Parameter Data M

In this mode, CH Comm waits for bytestreams containing a parameter and the corresponding data.

To use the Parameter mode, set Inputmode to 2.

The bytestream is a fixed length string of 50 bytes. The structure of the bytestream is described in the table below:

| Start | Length | Data | Description | Remark |
| --- | --- | --- | --- | --- |
| 1 | 1 | BOF | Start of message | Default: underscore. Can be adapted |
| 2 | 3 | Parameter | Parameter | See below for a list of valid parameters |
| 5 | 34 | Data | Data to send | Data format is the same than for Output mode. Must be padded to have a 34-bytes length. |
| 39 | 11 | Reserved | Not used |  |
| 50 | 1 | EOF | End of message | Default: underscore. Can be adapted |

The list of the parameter and corresponding data is described hereunder:

| Parameter | Data |
| --- | --- |
| 1 | FSTime |
| 2 | Coordinate |
| 3 | MSL |
| 4 | AGL |
| 5 | Pitch |
| 6 | Bank |
| 7 | Heading |
| 8 | Speed (Read-Only) |
| 9 | Vspeed (Read-Only) |
| 10 | Elevator |
| 11 | Aileron |
| 12 | Rudder |
| 13 | Elevevator Trim |
| 14 | Aileron Trim |
| 15 | Rudder Trim |
| 16 | Flaps |
| 17 | Spoiler |
| 18 | Gear |
| 19 | Brakes |
| 20 | Lights |
| 21 | Pitot |
| 22 | Comm |
| 23 | Nav1 |
| 24 | Nav2 |
| 25 | ADF |
| 26 | XPDR |
| 27 | Marker (Read-Only) |
| 28 | Autopilot |
| 29 | Throttle |
| 30 | Prop |
| 31 | Mixture |
| 32 | Magneto |
| 33 | EngValuesProp (Read-Only) |
| 34 | EngValuesJet (Read-Only) |
| 35 | Fuel |

The data format is the same as for the Output mode.

Read-only data are never part of the input bytestream.

Individual parameters in the ini-file are not used.

Input in Parameter mode bytestream sample:

Request "Gear down" and "Full flaps"

_018163830000000000000000000000000000000000000000_

_016163830000000000000000000000000000000000000000_

#### FSUIPC mode

In this mode, CH Comm waits for bytestreams containing a data length, an offset and the corresponding data.

To use the FSUIPC mode, set Inputmode to 3.

In this mode, you are not limited to the list of parameters provided by CH Comm. You can use all data that can be accessed by FSUIPC.

To use this mode, you must have know how to program with FSUIPC. More info can be found in the FSUIPC Software Development Kit available from Pete Dowson’s web site.

Individual parameters in the ini-file are not used.

The bytestream is a fixed length string of 30 bytes. The structure of the bytestream is described in the table hereunder:

| Start | Length | Data | Description | Remark |
| --- | --- | --- | --- | --- |
| 1 | 1 | BOF | Start of message | Default: underscore. Can be adapted |
| 2 | 1 | Data length | Number of byte to read | Valid: 1, 2, 4, 8 |
| 3 | 10 | Offset | Offset for FSUIPC | Alphanumeric: hexadecimal value |
| 13 | 15 | Data | Data to send to FSUIPC | Value that FSUIPC must receive. Decimal separator is always "." (dot). First byte can be "+" (plus) or "-" (minus). The full length must be a valid number. |
| 28 | 2 | Reserve | Not used |  |
| 30 | 1 | EOF | End of message | Default: underscore. Can be adapted |

Input in FSUIPC mode bytestream sample:

Request Comm frequency 127.30

_2000000034E00000000001003200_

## CH Comm.Ini-file

CH Comm uses an ini-file to specify all its parameters.

The CHComm.ini-file must be located in the same folder as the CHComm.exe file.

It contains the following sections:

[Timer]

Timer=500

Defines the rate for sending info in milliseconds.

Valid range: 200 to 60000 (0,2 sec to 1 minute)

If the setting is invalid, CH Comm defaults to 500

[ComSettings]

Port=2

Defines the port comm for sending info.

Valid range: 1 to 4

If the setting is invalid, CH Comm defaults to 2

Baud=14400

Defines the baud rate.

Valid settings: 110,300,600,1200,2400,9600,14400,19200,28800,38400,56000,128000,256000

If the setting is invalid, CH Comm defaults to 14400

Parity=N

Defines the parity.

Valid settings: E,M,N,O,S for Even, Mark, None, Odd, Space

If the setting is invalid, CH Comm defaults to N

DataBit=8

Defines the number of data bits.

Valid settings: 4,5,6,7,8

If the setting is invalid, CH Comm defaults to 8

StopBit=1

Defines the number of stop bits.

Valid settings: 1,1.5,2

If the setting is invalid, CH Comm defaults to 1

BOF=95

Defines the ASCII code of the first character of the data string.

Valid settings: 0 to 255

If the setting is invalid, CH Comm defaults to 95

EOF=95

Defines the ASCII code of the last character of the data string.

Valid settings: 0 to 255

If the setting is invalid, CH Comm defaults to 95

CHVersion=3

Defines the version of the data structure (for downward compatibility)

Valid settings: 3 (in version 3)

If the setting is invalid, CH Comm defaults to 3

Inputmode=1

Defines the type of input mode

Valid settings: 1,2,3

1: full input mode

2: parameter input mode

3: FSUIPC mode

If the setting is invalid, CH Comm defaults to 1

[Situation]

FSTime=1

Coordinate=1

MSL=1

AGL=1

Pitch=1

Bank=1

Heading=1

Speed=1

VSpeed=1

[Controls]

Elevator=1

Aileron=1

Rudder=1

ElevTrim=1

Flaps=1

Spoiler=1

Gear=1

Brakes=1

Lights=1

Pitot=1

[Radio]

Comm=1

Nav1=1

Nav2=1

ADF=1

XPDR=1

Marker=1

[Autopilot]

AutoPilot=1

[Engines]

Throttle=1

Prop=1

Mixture=1

Magneto=1

EngValuesProp=1

EngValuesJet=1

Fuel=1

Defines the data to be sent and/or received.

Valid settings: 0,1,2,3

Valid settings for read only data: 0,1

0: data not exported

1: data exported

2: data imported

3: data exported and imported

If the setting is invalid, CH Comm defaults to 1

# CH Comm Clients

Included in the archive is some sample source code for client-applications.

None of these samples are to be considered fully operational software. They are just basic samples.

They can be used as starting points for custom development.

# Credits

Many thanks to:

Peter Dowson: for developing the FSUIPC

The members of the Flight Simulator Club Belgium: for beta-testing the CH Comm.

Sven Aelterman, member of the Flight Simulator Club Belgium: for reviewing this document.

# Disclaimer

CH Comm comes with no warranty or claim of fitness or reliability.

CH Comm is distributed AS IS, USE AT YOUR OWN RISK. The author of CH Comm has absolutely no affiliation whatsoever with Microsoft® Corporation. Neither the author of CH Comm, nor Microsoft® Corporation shall be held responsible for any loss of data, downtime, loss of revenue or any other direct or indirect damage or claims caused by CH Comm or FILES USED IN CONJUNCTION with CH Comm.

# Redistribution Terms

CH Comm is FREEWARE, and:

- MAY NOT BE sold.

- MAY NOT BE uploaded to, nor archived in, BBSs and web sites which charge file download fees.

- MAY NOT BE uploaded to, nor archived in, BBSs and web sites which are partly or wholly beneficially owned or operated by a commercial enterprise which is engaged in the sale of computer hardware or software.

- MAY NOT BE redistributed with computer hardware or software for which money is charged.

- MAY NOT BE redistributed by a commercial publisher in any form or under any pretext. This prohibition includes but is not limited to floppy disks and CD-ROMS distributed with magazines or books.

- MAY NOT BE redistributed on floppy disk, CD-ROM, nor in any other printed or electronic storage form for which money is charged, nor as part of a package for which money is charged. This prohibition includes but is not limited to any form of redistribution for which any type of materials or handling fees are charged.

- MAY NOT BE disassembled, decompiled, decomposed, decoded, nor reverse engineered.

Subject to the exclusions listed above, the archive containing CH Comm may be uploaded to BBSs and web sites and otherwise redistributed on a FREEWARE basis as long as the original contents are not modified in any way.

THERE ARE NO EXCEPTIONS to the redistribution terms stated above without the prior written permission of the author.

# Copyright

CH Comm carries the following copyright:

Copyright (C) 1998-2001 by Claude Hanssens. All rights reserved.

Microsoft® is a registered trademark of Microsoft® Corporation.

Flight Simulator is a trademark of Microsoft® Corporation.

FSUIPC.DLL has a copyright (C) 1999-2001 by Peter Dowson.